## Slide 1: Nuclear Imaging I (SPECT)
RT4220 – Lecture #12
Kedree Proffitt
WSU
10/27/2025

## Slide 2: Basics of Nuclear Medicine
Patient presents with a disease  suspected disease can be imaged with a particular radioactive tracer  radioactive tracer is injected  an image is formed of the disease by a machine
The underlined section is the only difference between gamma cameras, single photon emission computed tomography (SPECT), positron emission tomography (PET), and now Compton cameras
All nuclear medicine detectors are either scintillator or semiconductor based
Nuclear imaging permits functional imaging, exceptionally important!

## Slide 4: Modes of Nuclear Imaging I
Gamma Camera
  Planar images via projections
  Typically scintillators and PMTs
  Physical collimation
  Uses low-energy photon emitters
SPECT
  Tomographic imaging (3D) via step-and-shoot planar images
  Typically scintillators and PMTs
  Physical collimation
  Uses low-energy photon emitters

## Slide 5: Modes of Nuclear Imaging II
PET
  Intrinsically tomographic data (3D)
  Typically scintillators, but moving towards semiconductors
  Electronic collimation
  Uses positron emitters (high-energy photons)
  Generally better spatial resolution and sensitivity than SPECT
  Functional imaging

## Slide 6: Gamma Camera Basics
Injection
Gamma photons generated by beta- emitter or Tc-99m
Photons leave patient and pass through collimator
Remaining photons are scintillated (each keV produces roughly 38 low energy photons in the visible band for NaI(Tl))
PMT converts scintillated photons into electronic signal
A pulse height analyzer rejects suspected non-valid events
A position logic circuit determines the origin location of each signal, now it is counted!
Many counts are summed together to form a planar image

## Slide 9: Step Three: Collimation
Parallel hole is most common in nuc. med.
Pinhole is used for thyroid uptake analysis
There are other forms of collimation that are gaining prominence, but are too complicated for us

## Slide 10: Step Four: Possible Photon Fates

## Slide 11: Step Six: Discrimination of Energy

## Slide 12: Step Seven: Event Localization

## Slide 13: Step Seven Continued

## Slide 14: Common Procedures
Ask the nuc. med. people what they see most (Almost all are Tc-99m based)
Bone Scans
  Cancer
  Occult Fractures
  Osteomyelitis/Arthritis
Cardiac Scans
Metastatic Cancer
Prostate Cancer
Neurological Scans

## Slide 23
Notes: Some new notes: Physicians HATE NOT HAVING A TRUE PLANAR IMAGE