## Slide 1: Nuclear Imaging II (PET)
RT4220 – Lecture #13
Kedree Proffitt
WSU
10/30/2025

## Slide 2: Basics of PET Imaging
Positron Emission Tomography  Positron  2x 511 keV photons oppositely opposed  near-simultaneous detection of each photon tells us where it came from  we can quantify how much tracer was deposited in a given location
Extremely short half-life of positron emitters:
  C-11: 20 mins
  O-15: 2 mins
  F-18: 110 mins
Short half life requires on-site production; we have a generator!
Most common PET radiopharmaceutical is FluoroDeoxyGlucose (F-18 != FDG)

## Slide 4: FDG Scans
Types of Scans:
  Tumor imaging and staging
  Detection of sub-clinical involvement
  Cardiac tissue viability studies
  Brain Imaging
Function:
  Localizes like glucose in the body but gets stuck

## Slide 7: Common PET Usage
Primarily to detect cancer and monitor its progression/metastasis status
PET/CT has become the primary imaging tool for cancer staging
  There are other great non-imaging tools!
Apparently, some are using PET to diagnose Alzheimer’s?

## Slide 8: Common SPECT Usage
SPECT primarily for tracking the progression of heart disease (blocked coronary arteries)
There are also radiotracers for detecting bone, gall bladder, and intestinal disorders
Apparently, some people have used it to help diagnose Parkinson’s?

## Slide 20: Other Nuclear Imaging
All the things I never saw

## Slide 22: I-131 Therapy
I-131 (administered orally) is intended for:
  Treating thyroid diseases (ie. hyperthyroidism: 4-10mCi)
  Treating thyroid carcinomas (100-150mCi)
  Post thyroidectomy or thyroid lobectomy (75-150mCi)
  Treatment of distant metastases (150->200mCi)
  Diagnostic studies (I-131: 4-10μCi or I-123: 100-200 μCi)
Therapeutic patients:
  Must avoid contact with pregnant women, infants and young children for a few days post treatment
  Should not sleep in the same bed with another person for a few days post treatment
Hospitals may quarantine therapeutic patients

## Slide 23: I-131 Therapy
Hospital room setup for a therapeutic I-131 patient

## Slide 24: I-131 Therapy
Beta minus decay
  8.01 day half life
  90% of Decays have:
    Max beta particle energy = 606.3keV
    Average energy of 190keV (~1/3 MaxE)
  Beta energy absorbed within 0.6 to 2.0mm of tissue thickness
~637 keV & 365 keV gamma emitted
  Can be used for imaging or uptake measurement
  I-131 is never used solely for diagnostic purposes

## Slide 25: I-131 Decay Chart

## Slide 26: I-123 Diagnostic Studies
I-123 has a short half-life (13.3hr)
  I-131 half-life was 8.01 days
  97% Beta Minus, 3% EC
  Emits 159keV gammas
  Allows for much lower dose to patient
Patient studies are performed 6-24hrs after ingestion
  Allows time for accumulation in the thyroid
Gamma camera’s NaI detector is efficient due to the 159keV photons that emitted

## Slide 27: I-123 Diagnostic Studies
Thyroid uptake study:
  Determine thyroid functionality by counting how much radioactivity is taken into the thyroid
  Normal uptake = 15-25%
    Hypo: <10%
    Hyper: >30%
  Performed using a gamma camera with a pinhole collimator or a scintillation detector called a “thyroid probe”

## Slide 28: I-123 Diagnostic Studies
Imaging with Gamma Camera
  Used to find abnormalities in absorption and uptake of iodine in the thyroid
Thyroid Uptake Probe
  Scintillation counting system
  Used to find uptake of iodine
  in the thyroid
  Images are not created with the
  uptake probe

## Slide 29: Iodine Thyroid Uptake Study

## Slide 30: Theranostics
Thera(-peutic / Diag-)nostics
Links radionuclides to specific receptors
  SSTR2 – Somatostatin Receptor
    Expressed in NETs
      NeuroEndocrine Tumors
Ga-68 is a positron emitter (PET)
Lu-177 DOTATATE = “Lutathera”
Notes: Gallium-68 is used for cancer detection

## Slide 31: Current Theranostic Treatments of Interest
Xofigo: Ra-223 Dichloride
  Bone Metastases following Prostate Cancer
Unnamed: Lu-177 PSMA
  Prostate-Specific Metabolic Antigen
Lutathera
  GEP (Gastroentero-pancreatic)-NETs
SIR-Spheres & TheraSphere: Y-90 MicroSpheres
  HCC (Hepatocellular Carcinoma, a liver cancer)
Ac-224 PSMA
  Alpha emitter

## Slide 32: Trends in Theranostics
What kind of tumors?
GEP-NET’s (small percentage)
Prostate
  You’ll probably have to work with these someday

## Slide 33: Typical workflow in Theranostics
Radiation Safety Protocol Development
  Transportation of drug from hot lab to clinic to storage
  Clinic safety
    Policies for the room
    Training of staff (physician through housekeeping)
  Patient education paperwork
Package Acceptance, Verification, and Storage
  Wipe test, check U/mCi, label for tx
Preparation of Drug for Delivery
In-Clinic Drug Delivery Assistance
Cleanup of Room, Radioactive Waste
Storage and Disposal of Radioactive Waste
All Text: What Physicists Do at KCI
Image from thebalancecareers.com

## Slide 34: Dosimetry in Theranostics
Xofigo: 1.49 uCi/kg of patient weight sent, delivered in syringe
Lu-177 PSMA: Measure out 200mCi in a 10cc syringe.
Lutathera: Standard dose of 200mCi sent in vial, delivered to all patients via gravity method
  Or, if you’re a maverick, via 60cc syringe and a chemotherapy pump