## Slide 1: Introduction to Brachytherapy
RT4220 – Lecture #15
Kedree Proffitt
WSU
11/13/2025

## Slide 2: What is Brachytherapy?
“Treatment with radionuclides at short distance”
From latin brachios, meaning short
This is in contrast to external beam therapy, or teletherapy
We can characterize the many modalities of brachytherapy as such:
  Method of placing sources
  Dose rate
  Loading technique

## Slide 3: Why is Brachy Used?
High dose to small volume
01
Less dose to superficial tissues
02
Shorter overall treatment time (days)
03
Radiobiological advantages of low dose rate (?)
04

## Slide 4: Where Brachy Fails
Radiation exposure to staff, visitors
Invasive procedure
Requires highly skilled operator
Requires hospital admission
Not suitable for large volumes
Precision of placement becomes critical

## Slide 5: Categories; by Method
Intracavitary: Applicator in a natural cavity
Gynecological
Interstitial: Needles, catheters, or seeds placed directly in tissue
Prostate, cervix, head and neck, breast, …
Surface: Applicator applied externally
Skin
Intraluminal: Tubes placed in tubular organs
Bronchus, biliary tree, esophagus, arteries

## Slide 6: Intracavitary

## Slide 7: Interstitial

## Slide 8: Surface

## Slide 9: Intraluminal

## Slide 10: Categories; By Dose Rate
Permanent: < 20 cGy/hr (natural decay)
Low Dose Rate (LDR): 30-80 cGy/hr (standard)
Medium Dose Rate: 100-1200 cGy/hr (has problems with radiobiology)
High Dose Rate (HDR): >1200 cGy/hr (fractionated)
Pulsed: many small HDR fractions, simulating LDR

## Slide 11: Categories; BY loading Method
Manual: “hot” loading in the OR
Manual Afterloading: unloaded applicator at surgery, sources placed later for continuous treatment
Remote Afterloading: source managed by machine, usually fractionated or interruptible

## Slide 13: Typical Activities Used
Radioactive Stent: uCi range
Permanent I-125: 0.4 mCi/seed, to 30 mCi
Temporary GYN: 25 mCi/source, to 200 mCi
Temporary Template: 3 mCi/seed, to 400 mCi
HDR: 10 Ci

## Slide 14: Types of Sources
Needles
Tubes
Wire
Seeds
Ribbons
Plaques
Pellets
Cable-mounted

## Slide 15: Important Fundamental Characteristics
Half-life
Mean Energy
HVL, TVL
Exposure Rate Constant ()
Exposure Rate Constant (Γ)
Half-life
Mean Energy
HVL, TVL

## Slide 16: Review of Fundamentals
GET PHYSICSED! :o

## Slide 17: Mean Energy
Photon emitting isotopes can be grouped into two categories:
  High Energy: >100 keV, similar to Radium in tissue, thus they have similar character in tissue, vary only in shielding characteristics
  Low Energy: <50 keV, isotopes like I-125 and Pd-103

## Slide 18: Exposure Rate Constant ()
Relates contained activity to an output
May describe exposure or air kerma
Source of error in traditional systems
Not used today to calculate dose, but physics still learns it

## Slide 19: Radioactive Decay and Activity
Activity: the number of nuclear disintegrations per unit time
Experimental Activity: proportional to the number of parent nuclei
Activity at a Given Time:
Half-life: expected time where half of the original activity will decay
Mean-life: the average lifetime of a given nucleus

## Slide 26: Load Up Brachytherapy Quality Assurance!
By Dr. Adrian Nalichowski