## Slide 1: Brachytherapy Calculations
RT4220 – Lecture #16
Kedree Proffitt
WSU
11/18/2025

## Slide 2: Additional Intro To Brachy Stuff
Have even more brachy!

## Slide 4: Historical Perspective
Initially most treatment techniques were developed with radium
Modern dosimetry is still associated with radium
Safety concerns about radium
  Radium decays to radon (a gas)
  In a sealed chamber (seed), gas builds up
    Gas leak
    Radioactive material dissemination
Artificial radionuclides are now used
  Useful energies for therapy treatments
  Convenient half-life’s

## Slide 5: Lower Lip Tumor (example)
53 year old patient
Surgery could remove tumor but the patient would lose partial function of the lip

## Slide 6: 7 Iridium-192 Needles
Custom plaque for inserting sources
Local anesthetic
6 day treatment

## Slide 7: One Month Later…

## Slide 8: Two Months Later…

## Slide 9: Four Months Later

## Slide 10: Dose Rate
Want to achieve maximum dose to tumor and keep acceptable toxicity to surrounding normal tissue
Depends upon:
  Number of sources
  Geometric distribution
  Volume of target tissue
  Radiobiology of tumor vs. normal tissues

## Slide 11: Dose Rate
The biological effectiveness depends upon dose rate
Long term effects (toxicities) also depend upon dose rate

## Slide 12: Radiobiology of Dose Rate
To increase the survivability of healthy cells one should try to:
  Reduce dose rate or
  Extend treatment
    This allows repopulation of healthy cells
    This is why HDR is fractionated
Notes: More complicated- low dose rate benefits late-reacting normal tissues more than cancers, so in theory low dose rate radiotherapy better.

## Slide 13: Radiobiology of LDR vs. HDR
α = unrepairable damage; β = repairable damage
α/β ratios determine the “bendiness” of the cell survival curve for a particular tissue under radiation

## Slide 14
Low /
High /

## Slide 15: Radiobiology of LDR vs. HDR
If the α/β of normal tissue is less than the α/β of a tumor, LDR is better
  Early responding tissues have a high alpha beta ratio
    Skin, bone-marrow, intestinal epithelium
    Rapidly dividing cells
  Late responding tissues have a low alpha beta ratio
    Spinal Cord, lung, kidney
  Most tumors have a high alpha beta ratio
  Some tumors have a low alpha beta ratio
    Melanoma, sarcoma, prostate, breast

## Slide 16: HDR vs. LDR
Comparing HDR to LDR
  Clinical outcome
  Toxicities
  Radiobiological effectiveness depends on tumor repair vs. normal tissue repair
Target for HDR
  Just be equal to LDR (does not have to be better) because of other benefits
    Increased patient numbers
    Outpatient treatment
Trend is moving toward HDR

## Slide 17: LDR Brachytherapy
Advantages
  Biological advantage for normal tissues vs. tumor tissues
  Does not require large amounts of shielding
Disadvantages
  Requires long time to deliver therapeutic dose
  Often requires hospitalization
  Limited number of patients can be treated

## Slide 18: HDR Brachytherapy
Advantages
  Short duration treatment time
  Increase patient population
  More precise dose distribution than LDR
    HDR often used as a boost or even primary treatment for prostate cancer
Disadvantages
  Dose to staff more of a concern
    Must use a remote afterloader
  Radiobiology can be an issue

## Slide 19: HDR Source
Iridium-192
  Small line source welded to end of a flexible drive cable
  Ir-192 source of 5-10 Ci provides a dose rate of 7Gy/min at 1cm from the source.
Source dimensions
  0.3 to 0.6 mm diameter
  3.5 to 10 mm long
Storage of source wire (when not in use)
  In shielded safe or vault (Tungsten or depleted uranium )
  1 mR/h at 10 cm

## Slide 20: Radioactive Source

## Slide 21: HDR Channels
HDR has several channels
Indexer system delivers sources from vault to channel
Applicators or catheters connected to channels
  Transfer tubes / guides
Dummy source wires used as QA to verify path is clear of obstructions

## Slide 22: Brachytherapy Calculations
Meat and… nay, but potatoes!

## Slide 23: Quantities For Source Specification
Aapp (Apparent Activity)
  Activity of an un-encapsulated source delivering the same activity as the encapsulated source
Exposure Rate
  Exposure rate constant “”
  Milligrams Radium equivalent (MgRaeq)
Sk: Air Kerma Strength (U, or μGy*m2 / hr)
  Kerma = Kinetic Energy Released in MAtter
  Reference energy transfer / dose rate currently used for source calibration and brachytherapy dosimetry
  Reference Air kerma rate measured at 1 meter in air

## Slide 24: Apparent Activity
Actual activity not particularly useful quantity because the source is encapsulated
Apparent activity
  Activity of an un-encapsulated source producing the same exposure as the encapsulated source
Allows the use of activity for dose calculation without explicit knowledge of source encapsulation

## Slide 25: Exposure Rate Constant ()
Tabulated constant
  Assigned to source based on ionization measured in air
Typical  units:
  R*cm2/(mg*hr), when working in “mg Radium”
  R*cm2/(mCi*hr)

## Slide 26: Exposure Rate Constant ()
= Exposure rate (R/hr, R/s, etc)
A = Apparent activity (Ci, mCi, Bq, etc)
 = Exposure rate constant
r = distance from source

## Slide 27: Radium-226
The curie is the historical unit for activity
  1 Ci = decays per second in 1g of radium
  1g radium ≈ 1 Ci = 3.7 x 1010 Bq (we now know that 1g of Radium measures closer to 0.98Ci)
  This is why we can have different units for GRa:
    GRa = 8.25 R*cm2/mCi*hr or
    Ra = 8.25 R*cm2/mg*hr

## Slide 28: Radium Equivalence
Older treatment protocols may call for a mass of Radium instead of exposure rate or dose
Other radionuclides may be substituted for Radium using exposure rate constants ()

## Slide 29: Common Exposure Rate Constants ()
Radionuclide  (R*cm2/mCi*hr)
Ra-226 8.25
Co-60 13.07
Cs-137 3.28
Au-198 2.327
Ir-192 4.62
Pd-103 1.48

## Slide 30: Radium Equivalence Ratios
Apparent Activity of isotope
Exposure Rate Constant of isotope
Exposure Rate Constant for Radium (Γra)
  mgRaeq = Aapp * Gx / Gra mgRaeq = * r2 / Gra

## Slide 31: Exposure to Dose Rate: Air Kerma Strength
Now relate exposure in air (X) to dose
  Can get Exposure from Activity, Distance, Time and the Exposure rate constant
KERMA
  Kinetic Energy Released per unit Mass
    All KE given to charged particles from uncharged particles
  Proportional to Dose

## Slide 32: Kerma
Indirectly ionizing radiation (photons and neutrons) deposit energy:
  Kinetic energy imparted to electrons/nuclei is then deposited as dose downstream

## Slide 33: Exposure to Dose Rate: Air Kerma Strength
Air Kerma:
K = X (W/e)
  X = exposure [R]
  (W/e) = average energy to create ion pair [J/C or eV/i.p.]
Air Kerma Strength: Sk = dK(r)/dt * r2
    Change in Air Kerma per unit time * area
    Units of “U” [μGy*m2/hr] or [cGy*cm2/hr]
    Source with 1U produces:
      1cGy/h at 1 cm from source
      1μGy/h at 1 m from source

## Slide 34: Common Air Kerma Strength Conversions @ 1m
1U (μGy m2/h)
= 0.348 mCi for 137Cs
= 0.243 mCi for 192Ir
= 0.486 mCi for 198Au
= 0.787 mCi for 125I
= 0.773 mCi for 103Pd

## Slide 35: Air Kerma Strength – Why?
Source specification
TG-43:
Don’t panic I won’t test you too hard on this…
Accounts for variations due to dose distribution, drop off, absorption, scatter, filtration, geometric effects for any point.
Dose rate at a point
Dose rate constant
Air Kerma Strength

## Slide 36: Important Calculation Definitions
Poke ya prostate, Yank ya Uterus