## Slide 1: Review of Radiation Physics
RTT4220 – Lecture #1
Kedree Proffitt
WSU
09/02/2025

## Slide 2: Review of Electricity and Magnetism
The old stuff
Notes: Common E&M Derived Values
Common Electricity Equations
Acceleration of Electrons
Atomic Mass Units

## Slide 3: Electricity and Magnetism
Energy (Many Symbols) [J or eV]
Charge () [C or As]
Current () [A]
Electric Potential (Voltage) () [V or J/C]
Power () [W or J/s]
Resistance () []

## Slide 4: Moving Electrons
When electrons accelerate  photons are generated
Acceleration can occur two ways; SPEED or DIRECTION
High speed accelerating electrons are awesome and dangerous: X-rays
We often want fast electrons, easiest way to get them is VOLTAGE
VOLTAGE gives electrons energy, makes them accelerate (charged particles)

## Slide 5: Electron Energy and Speed Practice
An electron travels a 300 V electric potential ( V) has a typical mass ( kg) and a typical charge (); find the kinetic energy assuming it started at rest.
Now find the velocity it had as it left the potential (ignore relativity).

## Slide 6: Atomic Mass Units
An atomic mass unit (amu) is 1/12th of the mass of a carbon-12 nucleus.
Carbon-12 has 6 protons and 6 neutrons and weighs 12 amu (by definition).
Protons and neutrons weigh ~ the same, each is about 1 amu
1 amu = 1.66E-27 kg

## Slide 7: Radiation Physics
The good stuff
Notes: What is Radiation
Types of Radiation
What is a photon
Photon Spectrum
Clearing up Photon vs Gamma vs Xray
Wave-Particle Duality
Common Photon Units
Calculating Photon Chars.

## Slide 8: What is Radiation?
When energy radiates away from something (energy or mass)
Lots of misconceptions!
Many types of radiation and the uses/danger are just as variable
Light, Microwave, infrared, alpha, beta, gamma, the list goes on

## Slide 9: Types of Radiation
ELECTROMAGNETIC
Photons (that’s it!)
The name depends on energy and/or source (i.e. Gamma/X-ray/Light)
PARTICULATE
Helium (Alpha)
Electrons (Beta)
Protons

## Slide 10: What is a Photon?
All EM radiation is comprised of photons ()
Because of dumb history photons were “discovered” many times before we unified them thus some names stuck
This yields the ELECTROMAGNETIC SPECTRUM
If it came from an atom*:
ITS GAMMA RADIATION*
If it came from anything else*:
WE DON’T HAVE A WORD*
But no matter what, it’s on the spectrum!

## Slide 11: Electromagnetic Spectrum

## Slide 12: Wave-Particle Duality
EM Radiation behaves in ways that determine it MUST BE particles, and it MUST BE waves at the same time.
?????
Its both due to quantum mechanics.
Wave-like Behavior:
Particles CANNOT diffract
We see EM rad. diffract!
Therefore, its wave-like!
Particle-like Behavior:
Waves CANNOT deposit energy in “batches”
EM rad. does so: photoelectric effect
Therefore, its particle-like!

## Slide 13: Wave-Particle Duality
Wave-Like
Particle-Like

## Slide 14: Photon Physics
Photons are the representation of the particle-like behavior
Photons travel at the speed of massless things*
Photon energy is directly related to its wave-like behavior frequency
EM frequency is inversely related to its wavelength
( [Js] is Planck’s constant)

## Slide 15: Photon Energy Practice
An x-ray with a wavelength of 4.20E-9 m is ATTENUATED by a detector. How much energy would be deposited? What is the frequency of that radiation?
How much energy would be deposited by 1 MILLION of these x-rays?